## Slide 1: Kinect Open Source Programming Secrets
Andrew Davison
Prince of Songkla University
Thailand
ad@fivedots.coe.psu.ac.th
Hacking the Kinect with OpenNI, NITE, and Java

## Slide 2: Overview
using OpenNI
using NITE
as an input source to other libraries
http://fivedots.coe.psu.ac.th/~ad/kinect
Eight examples (if I have time)
1. The Kinect Sensor
2. Maps
3. Skeletons
4. Hand Points and Gestures
5. Computer Vision
6. Augmented Reality
7. Summary

## Slide 3: 1. The Kinect Sensor
used for 3D
depth sensing
CMOS color sensor
(for RGB imaging)
motorized
tilting base (up/down ~30)
three microphones (downward facing)
IR light
source
CMOS IR
sensor
status LED
three-axis
accelerometer
one microphone (downward facing)

## Slide 4: 2. Depth, Image, IR Maps
The IR light emits a fixed pattern of spots (randomly distributed)

## Slide 5: Map Generation
Depth Generator
Depth
Map
repaint
read map
wait on context update
initialize context
and generator(s)
Image
Generator
Image
Map
IR
Generator
IR
Map
OR
OR
camera
image

## Slide 6: Initialization
Context context = new Context();
License license = new License("PrimeSense", "0KOIk2JeIBYClPWVnMoRKn5cdY4=");
context.addLicense(license);
DepthGenerator depthGen = DepthGenerator.create(context);
MapOutputMode mapMode = new MapOutputMode(640, 480, 30); // xRes, yRes, FPS
depthGen.setMapOutputMode(mapMode);
context.setGlobalMirror(true);
context.startGeneratingAll();

## Slide 7: Wait, Read, Repaint Loop
while (isRunning) {
try {
context.waitAnyUpdateAll();
}
catch(StatusException e)
{ System.out.println(e);
System.exit(1);
}
updateDepthImage(); // my code
repaint();
}
try { // close down
context.stopGeneratingAll();
}
catch (StatusException e) {}
context.release();

## Slide 8: OpenNI Generators
primarily used
by middleware (e.g. NITE)

## Slide 9: 2.1. Transforming the User
later
The transformation is applied to all of the camera image,
but transparent parts of the changed image aren't visible.

## Slide 10
cycle through blurring
Time-based changes
Center-of-mass (CoM) based changes
change stays
centered on
user

## Slide 11: Building the Scene
Depth Generator
Image
Generator
set alternative
viewpoint
for real world
coordinates to 2D
(projective)
mapping
User
Generator
Scene
MetaData
scene map
(user ID map)
remove
background
camera
image
CoMs of
user IDs
(optional)
Java 2D filterOp
http://www.jhlabs.com/ip/filters/

## Slide 12: Panel Execution
repaint
update
wait on context update
initialize context
and generator(s)
remove background of camera image;
apply filterOp (optionally based on time and CoM of user)
draw background image
draw camera image;

## Slide 13: 3. OpenNI Skeleton
There are 15 joints (and 9 more that are not currently initialized by the skeleton capability).
On-screen view,
with mirroring
enabled

## Slide 14: 3.1. Heads and Backgrounds
switch heads and backgrounds
(via keyboard or dialog selection)

## Slide 15: Generators (and Capabilities)
Depth Generator
Image
Generator
set alternative
viewpoint
for real world
coordinates to 2D
(projective)
mapping
User
Generator
Skeleton
Capability
Pose
Capability
Scene
MetaData
listeners
for various
user events
:
:
camera image
scene map
(user ID map)

## Slide 16: Rotating the Head Image
Calculated using
the head and neck
coordinates.

## Slide 17: 3.2. Viewing Users in 3D
joints and limbs
for each
user
rendered using Java 3D

## Slide 18: Creating a Skeleton
Depth Generator
for real world
coord to 2D
(projective)
mapping
User
Generator
Skeleton
Capability
Pose
Capability
psi pose
detected
calibration
completed
new user
lost user
user has
exited
user has
reentered
calibration
starting
add a
Skeleton
object to
the 3D scene

## Slide 19: Overview
using OpenNI
using NITE
as an input source to other libraries
1. The Kinect Sensor
2. Maps
3. Skeletons
4. Hand Points and Gestures
5. Computer Vision
6. Augmented Reality
7. Summary

## Slide 20: 4. NITE Hand Points and Gestures
NITE gestures are derived from a stream of hand points which record how a hand moves through space over time.
Gesture detectors are sometimes called point listeners (or point controls) since they analyze the hand points stream looking for gestures.

## Slide 21: NITE Gesture Classes

## Slide 22: 4.1. Gesture GUIs (GGUIs)

## Slide 23: Controlling the GGUIs
Depth Generator
Image
Generator
for coords mapping
Point
Control
new hand point (P1)
for camera image
Hands
Generator
Gesture
Generator
Session
Manager
hand point moved (P2)
no active hand points (P3)
session ended (S)
update GGUI
deactivate GGUI

## Slide 24: Overview
using OpenNI
using NITE
as an input source to other libraries
1. The Kinect Sensor
2. Maps
3. Skeletons
4. Hand Points and Gestures
5. Computer Vision
6. Augmented Reality
7. Summary

## Slide 25: 5. Computer Vision and the Kinect
Use the Kinect sensor as input to JavaCV (a Java binding for OpenCV)
  input can be RGB and/or depth reading
Current and past (student) projects:
  motion detection
  face detection & recognition
  eye tracking
http://opencv.willowgarage.com

## Slide 26: 5.1. Hand Recognition

## Slide 27: From OpenNI to OpenCV
Depth Generator
Depth
Map
threshold
smooth
largest
contour

## Slide 28
start pt
end pt
depth pt
depth
convex hull
largest contour
convexity defects
each defect is a tuple:
(start pt, end pt, depth pt, depth)

## Slide 29
start pt
end pt
depth pt
depth
simplified
convexity defects
remove defects with:
shallow depths
small angles between the start and end pts

## Slide 30: Finger Labeling
center of
gravity (cog)
angle to
the horizontal
rotate hand image to match predefined hand 'parameters'
thumb
index
middle
ring
little
fragile, hacky

## Slide 31: Uses?
move
finger rotate
zoom/pinch
double tap
multi slide
wave
hold
pick & drop
cluster & move
zoom spot
hold & tap
rotate two
cover
hide

## Slide 32: 6. Augmented Reality (AR)
A combination of a real scene and virtual elements generated by the computer.
Uses the Kinect camera as input to NyARToolkit
http://nyatla.jp/nyartoolkit/wp/?page_id=198

## Slide 33: Using NyARToolkit and Java 3D
search for
Hiro marker
using NyARToolkit
calculate
its position
and orientation
apply position
and orientation
to marker model
render model
in front of the
video frame
using Java 3D
video stream
from the Kinect
Image
Generator

## Slide 34: The User's Viewpoint
background
+ Z
+ Y
+ X
model

## Slide 35: 7. Summary
OpenNI
  RGB, depth, IR maps
  skeletal tracking, scene/user IDs
NITE
  hand points, hand gestures
7 Examples
  aligned maps
  user transformation
  heads & backgrounds
  3D users
  gesture GUIs
  hand recognition
  augmented reality (AR)

## Slide 36: Topics not Discussed
Tilt motor, LED, accelerometer
  easy to add using LibusbJava
Audio source input, speech recognition, beamforming
  using MS Kinect audio driver, JSAPI, TalkingJava,
Motion detection, face recognition, eye tracking
Multiple-marker AR
Games – Kinect breakout
θ
right
left
positive
negative

## Slide 37: More Information
All the code, draft chapters, and extra examples, are available at my website:
  http://fivedots.coe.psu.ac.th/ ~ad/kinect/

## Slide 38: One last example...

## Slide 39: 8. Where I work...
I'm an Ajarn (lecturer) in the Department of Computer Engineering (CoE), Faculty of Engineering, Prince of Songkla University (PSU)
I'm based at the Hat Yai campus, Songkhla province, in the south of Thailand.

## Slide 40: PSU at a Glance...
1st university in Southern Thailand, est. 1967
5 campuses
39,000 students (2012)
Hat Yai
Trang
Pattani
Phuket
Surat Thani

## Slide 41
Prince of Songkla University
(PSU), Hat Yai campus
Department of
Computer Engineering (CoE)
Faculty of Engineering

## Slide 43: Department of Computer Engineering (CoE)

## Slide 44: PSU Academically...
A National Research University (NRU)
Ranked 4th in the Nation in terms of publications
Research strong points include:
  Natural rubber
  Biodiesel and energy
  Sea food and Halal food
  Marine sciences
  Nanotechnology
  Peace studies

## Slide 45: CoE Research Groups and Interests
Center for Network Research (CNR)
Wireless Sensor Network (WSN)
ANW Informatics Laboratory
Intelligent System (iSys) Research Team
  Computer Control and Robotics
  Computer System Design and VLSI Design